#### FREQUENCY RESPONSES OF FILTER FP-433

2          1.0 dB/div

(           0.0000  dB		REF     -7.238 dB

CENTER   0.070000000  GHz			SPAN   0.007000000  GHz

a

3          50.0   ns/div			S21                              -((/((

(           2.8659 ns			REF     49.0 ns

CENTER   0.070000000  GHz			SPAN   0.007000000  GHz

b

2        10.0   dB/div			S21                              log  MAG

(          0.0003  dB			REF   -7. 235  dB

CENTER   0.070000000  GHz			SPAN   0.030000000  GHz

c

1        10.0   dB/div		S21                             log  MAG

(          -7.2402  dB		REF   - 7.24 dB

START   0.035000000  GHz			STOP   0.150000000  GHz

d

Measured frequency response of 70/5 MHz filter, code FP-433:

(F0=69.9 MHz, BW3=5.0 MHz, BW40=7.9 MHz, IL=7.2 dB, AR=0.5, GDT=110 ns, UR=45 dB).

Structure:			Q-SPUDT + Q-SPUDT

Wafer:				LiNbO3, cut YZ; TCD= ( 86 ppm/oC.

Package: 		SMD 13.3x6.5x1.8 mm, IRK 12F2-5857C-C, NTK, Japan.

Source / Load impedance: 	50 Ohm single + L1C1 / 50 Ohm single +L2.

### MATCHING NETWORK OF FILTER FP-433

(in package SMD 13.3x6.5x1.8 mm, IRK 12F2-5857C-C, NTK, Japan)

L1*=135 nH; L2*=115 nH

C1*=10 pF

Q1=60; Q2=60

1. L1*, L2* - inductors with quality factor Q  60,  SMD type: SM-1206 ,NEOSID, Germany. Value of inductances are  selected in limits L1*=135(10 % nH and 
L2* =115(10 % nH depends on  capacity of the printed-circuit-board ( PCB ).

2. Input: (6-d); output: (12-j).

3. The mark  on the lid of package  opposite to contact pad  No "1".

4. An ultimate rejection in wide frequency range is depended on cross-talk in Customers PCB. Therefore PCB pattern shall be allows to obtain –(60-70) dB of electromagnetic signal level or better.

70_5.0S21match.doc

30-Jan-04