a

b

c

d

Measured frequency responses of AMPS 881.5 MHz filter Rx, code FP-582:

(F0=881 MHz; BW2.7=26.2 MHz - relative level 0 dB; BW3=28.5 MHz; IL=2.0 dB; UR=53 dB).

Structure: Two cascades LCRF.

Wafer: LiTaO3, cut yxl/42o; TCD=-28 ppm/oC.

Package: SMD 3.0x3.0x1.4 mm, KD-V99D59-A, KYOCERA, Japan.

Source/Load impedance: 50 Ohm single / 50 Ohm single without matching

881v4S21expMR.doc

23-Dec-02