| S21 |, dB

Frequency, MHz

a

| S21 |, dB

Frequency, MHz

b

| S21 |, dB

Frequency, MHz

c

Measured frequency response of 1960 MHz PCS filter, code FP-642 :

(F0=1960 MHz, BW3=52 MHz, BW30=150 MHz, IL=2.1 dB, UR=28 dB).

Structure:			6 resonators ladder filter.

Wafer:				LiTaO3, cut yxl/42o; TCD=-30 ppm/oC.

# Package:			SMD 3.0 x 3.0 x 1.3 mm.

Source / Load impedance: 	50 Ohm single / 50 Ohm single without matching.

1960v21S21exp MR.doc

24-12-03